Instructions to participants for the interlaboratory study:

Specific Migration on Food Contact Materials iis15P10SM

*	Please confirm sample receipt as soon as you have received and checked the contents of this package, preferably using the sample receipt confirmation form that you received together with this package.

Please complete the form and send it to iis (email iisnl@sgs.com or faxno. + 31 181 694543).

* 	This interlaboratory study concerns a plate of a material (PVC) that is to be used in food industry (e.g. in some piping) and therefore the specific migration should be limited. The material will be used many times. Each participating laboratory receives one plate of this material for the determination of the specific migration of Di(2-ethylhexyl)phthalate (=DEHP), by total immersion. Please note that the size of the plate is sufficiently large (18 x 15 cm) to give 2-4 samples with a surface area > 100 cm2 after cutting in 2 or 4 pieces. Please treat the sample as it was a routine sample and analyse it in the way you normally do in day-to-day circumstances.

*	Please take care to use during this PT the fixed test conditions as given in below table:

| Plate (PVC) | 1 piece, containing DEHP. |
| --- | --- |
| Simulant | 50% Ethanol |
| Exposure time | 1 hr (60 minutes) |
| Exposure temperature | 60.0 °C |
| Migration method | Total Immersion |
| Simulant volume | as per method used (please report volume in additional questions) |

*	Please report your test results via www.kpmd.co.uk/sgs-iis-cts/. Login details have been sent to you, but also can be requested via an email to iisnl@sgs.com.

# *	On the report page is a column, titled ‘reference method’. In case a method is mentioned in this column, it will be used for the calculation of the z-scores. It is of utmost importance to know that it is NOT mandatory to use this ‘reference method’ as test method. When you normally (routinely) use a test method other than the reference method, please select the method that you used under ‘Actual Method Used’. When your method is not mentioned under ‘Actual Method Used’, please select ‘Other’ and write the method that you used in the comments.

*	Please report the analytical results using the indicated units. Report in the last column the analytical results, rounded in accordance with the standard method that was used. Report in the first result column the same analytical results but less rounded (we suggest to report one extra significant figure) in order to give more meaningful statistical calculations. For example, when you use EN13130 for the determination of Specific Migration and you found a result of 10.614 mg DEHP/dm2, we request you to report 10.6 mg DEHP/dm2 in accordance with EN13130 and 10.61 mg DEHP/dm2 as ‘unrounded’ result, but reporting 10.614 mg DEHP/dm2 will also be OK.

* 	Please enter also the requested test details under ‘Additional Questions’.

# *	Within a time frame of one month test results can be entered or revised. It is not needed to enter all test results in one session. Within this one month you can add (or delete) test results and/or change test results or units.

*	The official closing date for reporting test results for this PT is October 9, 2015.

*	After the official closing date it is no longer possible to enter or correct test results via the data entry website www.kpmd.co.uk/sgs-iis-cts/. However, it is still possible to download the Word report form (incl. instructions) from our internet site www.iisnl.com. In the case you cannot report via the website or for unforeseen reasons cannot report before the closing date, please send the completed Word document via email to iisnl@sgs.com or by fax to +31 181 694543.

*	If you have any remarks/questions please contact:

ing. R.J. Starink, Institute for Interlaboratory Studies

P.O. box 200, NL-3200 AE Spijkenisse, The Netherlands

tel.no. +31 181 69 45 41      fax.no. +31 181 69 45 43

e-mail: iisnl@sgs.com           website: www.iisnl.com